## Slide 1: Rogue Access Points attacks
EVIL TWIN

## Slide 2: What is a rogue access point (AP)
A rogue access point is a wireless access point that has been installed on a secure network without explicit authorization from a local network administrator, whether added by a well-meaning employee or by a malicious attacker.
Think setting up a router in your dorm room

## Slide 3: Evil Twin

## Slide 4
“Starbucks Wifi” Channel 6
Rogue Access Point
“Starbucks WiFi”, Channel 6

## Slide 5
“Starbucks Wifi” Channel 6
Rogue Access Point
“Starbucks WiFi”, Channel 6

## Slide 6: Man in the Middle

## Slide 7: Advantages of Evil Twin Attacks
Relatively easy to perform
Hard to Detect
Targeted attack
  Doesn’t pwn everything in the area

## Slide 8: Disadvantages of Evil Twin
Doesn’t work against protected network out of the box
Workaround
  Listen for probe requests
  Identify ESSID and Channel of network that client have in common
  Spin up twin with ESSID and Channel
  Deauthorize secure network

## Slide 9: Detecting Evil Twins with Whitelisting
Whitelist all legitimate access points by bssid and mac address
Sniff continuously for probe responses
If probe response of essid, and the bssid is not in the whitelist, then it’s a rogue AP
Deauth rogue AP

## Slide 10
“I have ESSID ‘Starbucks’”
IDS
IDS
IDS
IDS
Is 11:22:33:44:00 Allowed?
Whitelist:
00:11:8A:B7:9F
22:33:44:55:66
99:99:99:99:66
Whitelist:
00:11:8A:B7:9F
22:33:44:55:66
99:99:99:99:66
No
Deauth
Find a sys admin

## Slide 11: Can spoof BSSID/mac
Rouge AP can be set up with same BSSID and MAC.
For all intents and purposes looks exactly like legitimate AP

## Slide 12: Other methods?
Detect using varying signal strength.
Establish baseline and check if it varies much.
  Note if the hacker figures out the signal strength you can modify it on a wireless card
  “iwconfig wlan0 txpower 30”

## Slide 13: Karma Attack
Seeks out WiFi requests from nearby devices
Responds that it is the droid wireless signal they are looking for
Pwns all nearby networks

## Slide 14: Evil Twin DEMO

## Slide 15: Wireshark
Packet Sniffing
Uses PCAP files to see everything on the network
“Just look at it”™
Reason 1 for not doing anything important on insecure WIFI

## Slide 16: Wireshark Demo